## Slide 1
Exploring the chemical space boundaries of potential candidates in liquid chromatography using molecular descriptors
Alex Nikolopoulos
1st examiner: Saer Samanipour
2nd examiner: Bob Pirok
Daily Supervisor: Denice van Herwerden

## Slide 2
Non-targeted is our target!
Is it possible to reduce the number of possible candidates?
Validation
Models
Assessment
Possible candidates
Not possible candidates
Data
Validation
Workflow
LC-MS is the dominant technique used in NTA
Non-targeted workflows enable to create an unbiased overview of a sample
Due to the intrinsically high number of features, identification can be cumbersome as well as expensive!
Each feature has multiple possible candidates
2

## Slide 3
How can we predict the retention of a compound?
The retention time is greatly affected by the chromatographic conditions
Stationary phase
Mobile phase composition
Temperature
Retention time (tR) will vary
Not reproducible results
Small change in any LC parameter
Retention time inadequate for the study
The best way to normalize retention times is by using a retention index system
3

## Slide 4
How can we predict the retention of a compound?
Gas chromatography
n-alkane homologous series
Mainly used in GC column comparison and characterisation
Kovat’s retention index
n-alkylamide homologous series (C3-C14)
Used in metabolomic studies, since it is MS-compatible
18 computationally selected compounds (not part of a homologous series)
Novel retention index with a broader reference system
University of Athens (UoA) retention index
n-alkylamide retention index
Liquid chromatography
Liquid chromatography
4

## Slide 5
Number of N atoms, molecular weight
Which factors influence the retention index?
Retention indices are not influenced by the chromatographic conditions.
Therefore, ri is only affected by the compound structure!
Compound structure
Longest aliphatic chain, number of acidic groups, Crippen logP
Total molecular surface area, Petitjean shape index
Presence of SMARTS patterns
1D descriptors
2D descriptors
3D descriptors
PubChem fingerprints
PaDEL is a computational tool used to calculate 2756 descriptors given a single compound SMILES
5

## Slide 6
Descriptors acquisition
Training datasets
n-alkylamide: 1488 compounds and their experimental ri
UoA: 1816 compounds and their experimental ri
Dataset used for application
SusDat NORMAN: 95115 compounds
PaDEL was used to calculate the descriptors of these datasets
But can we use all 2756 descriptors provided by PaDEL?
6
Notes: Mention that we have two different systems here!

## Slide 7
Descriptors selection and normalization
3-fold calculation for the n-alkylamide dataset
High variation between the calculations
Training datasets
n-alkylamide: 1488 compounds and their experimental ri
UoA: 1816 compounds and their experimental ri
Dataset used for application
SusDat NORMAN: 95115 compounds
PaDEL was used to calculate the descriptors of these datasets
Descriptors selection
Unstable descriptors
Descriptors with missing values
1170 useful descriptors
Descriptors of different order of magnitude
7
Notes: Mention that we have two different systems here!

## Slide 8
Model development
Descriptors
n-alkylamide ri
UoA ri
Random forest model A
Random forest model B
80% of each dataset is used as the training set of each model
The remaining 20% is used as the test set for validation
The maximum features per tree was set to the number of descriptors used divided by 3 [1]
Random forest has three main hyperparameters to be tuned
The other two hyperparameters must be optimized to increase the accuracy of the model
1 Hastie, T.; Tibshirani, R.; Friedman, J. The Elements of Statistical Learning, 2nd ed.; Springer New York: New York, NY, 2009
8

## Slide 9
Model hyperparameters optimization
n-alkylamide dataset
UoA dataset
The hyperparameters were optimized to maximize accuracy and avoid overfitting
We have two models able to predict accurately the retention indices!
Optimization
 | n-alkylamide | UoA
No. of trees | 400 | 500
Sample per leaf | 4 | 4
9

## Slide 10
Models with reduced number of variables
However, using 1170 variables is computationally expensive, what if we use fewer descriptors?
Most important descriptors were found based on average variance reduction
New models were created with a small number of (the most important) descriptors
 | n-alkylamide | UoA
R2 | 0.73 | 0.77
We have two models able to predict accurately and fast the retention indices!
10

## Slide 11
Can our models give accurate predictions for any compound? What are the limitations?
No model based on a limited training set can function adequately for the compounds of the entire chemical space
The applicability domain (AD) describes the model limits and is calculated with the leverage
Applicability domain
The leverage measures the similarity of a compound compared to the training set
11

## Slide 12
Principal component analysis
How similar are the compounds of the training sets with the compounds of the NORMAN dataset?
The n-alkylamide training set shows low similarity to the compounds of the NORMAN dataset
The UoA training set covers a great portion of the chemical space
12

## Slide 13
Retention index assessment
Unsuitable for LC analysis in a C18 column
Compounds of extremely low ri
Compounds of extremely high ri
No retention on the stationary phase
Elution at t0
Strong adsorption to the stationary phase
Extremely long retention times
The descriptors of the lowest and highest points of each model were slightly changed over multiple iterations
The low and high extrapolation areas were set at the 95% quantiles
95% area
Can every compound be analyzed in a C18 column?
We have found the ri ranges in which the compounds cannot be analyzed in a C18 column!
13

## Slide 14
Overall assessment
Is every compound with “acceptable” retention indices compatible with a C18 column?
Applicability domain
Predicted ri assessment
AD (n-alkylamide)
AD (UoA)
ri (n-alkylamide)
ri (UoA)
Group A
AD (n-alkylamide)
ri (n-alkylamide)
Group B
AD (UoA)
ri (UoA)
Group C
AD (n-alkylamide)
ri (n-alkylamide)
Group D
AD (UoA)
ri (UoA)
Group E
AD (n-alkylamide)
AD (UoA)
Group F
Inside
Outside
Acceptable
Unacceptable
Let’s see how the NORMAN dataset is distributed into these groups!
14

## Slide 15
Overall assessment
AD (n-alkylamide)
AD (UoA)
ri (n-alkylamide)
ri (UoA)
Group A
AD (n-alkylamide)
ri (n-alkylamide)
Group B
AD (UoA)
ri (UoA)
Group C
AD (n-alkylamide)
ri (n-alkylamide)
Group D
AD (UoA)
ri (UoA)
Group E
AD (n-alkylamide)
AD (UoA)
Group F
15
We have the classification of the NORMAN compounds based on their compatibility with RPLC analysis in a C18 column!

## Slide 16
Distribution of the NORMAN dataset into assessment groups
AD (n-alkylamide)
AD (UoA)
ri (n-alkylamide)
ri (UoA)
Group A
AD (n-alkylamide)
ri (n-alkylamide)
Group B
AD (UoA)
ri (UoA)
Group C
AD (n-alkylamide)
ri (n-alkylamide)
Group D
AD (UoA)
ri (UoA)
Group E
AD (n-alkylamide)
AD (UoA)
Group F
7.2%
5.0%
19.9%
0.6%
0.1%
67.1%
16

## Slide 17
Assessment performance – Literature search
How well does our assessment function?
Selection of 5 compounds from each group
Literature search on the analysis of these compounds in a C18 column
 | True positive | True negative
Predicted positive | 8 | 7
Predicted negative | 7 | 8
A
B
C
D
E
F
17

## Slide 18
Assessment performance – Reverse literature search
What if we reverse our validation strategy?
Selection of 20 compounds from random scientific papers stating their analysis in a C18 column
Tracking these compounds in the NORMAN dataset and finding their assigned group
 | True positive | True negative
Predicted positive | 7 | 3
Predicted negative | 8 | 12
A
C
B
D
E
F
18

## Slide 19
Final remarks
19
A novel workflow was developed to explore the theoretical space of compounds compatible with RPLC analysis in a C18 column
The suggested assessment showed a 63% accuracy, based on cross-validation with reported data
What was achieved?
What are the potentials of this study?
The NTA suspect list could be shortened
This would result in less challenging identification
A flexible approach is provided which could incorporate more elements in future studies and further increase its capabilities

## Slide 20: Thank you for your attention!
Questions?
20

## Slide 21
ri explanation
Kovats index
n-alkane homologous series
Ii equals the retention index
t0 the measured dead volume
ti the measured retention time of the analyte
n the number of carbons of the species in the homologous series that elutes right before the analyte
tn and tn+1 the retention times of the species within the series that elute right before and after the analyte.
UoA index
21

## Slide 22
How does random forest regression work?
Var1 > a
Var2 > b
Var3 < c
Var2 < d
751
819
355
215
378
YES
YES
YES
YES
NO
NO
NO
NO
Every decision tree “asks questions” to the set of variables of every compound
Multiple decision trees are randomly created using different set of variables
The result of the random forest is equal to the average result of all the decision trees
Decision trees are the core of a random forest regressor

## Slide 23
Correlation matrices

## Slide 24
Partial Regression model – n-alkylamide dataset
Used descriptors | 
1 | MLogP
2 | CrippenLogP
3 | nC
4 | CrippenMR
5 | piPC3
6 | C2SP2
7 | piPC10
8 | MPC10
9 | piPC2
10 | PubchemFP11
11 | WTPT-5
12 | nBase
13 | MATS1e
R2 (training set) = 0.88
R2 (test set) = 0.73
Cross validation 5-fold average = 0.70

## Slide 25
Partial Regression model – UoA dataset
Used descriptors | 
1 | CrippenLogP
2 | nBase
3 | McGowan_Volume
4 | CrippenMR
5 | MLFER_L
R2 (training set) = 0.87
R2 (test set) = 0.77
Cross validation 5-fold average = 0.74

## Slide 26
Assessment – Calculation of extrapolation region
Adjustment of the descriptor matrix around the original values of the lowest and highest point of the training set
Calculation of every descriptor 95% range
Fitting a gamma distribution and defining the 95% area as the uncertainty range